## Slide 1: SUPERHETERODYNE RECEIVER
By Ahsanul Kobir Rashed
ID : 11709023

## Slide 2
In electronics, a super heterodyne receiver (often shortened to superhet) uses frequency mixing to convert a received signal to a fixed intermediate frequency (IF) which can be more conveniently processed than the original radio carrier frequency.
It was invented by US engineer Edwin Armstrong in 1918 during World War I.
At the cost of an extra frequency converter stage, the super heterodyne receiver provides superior selectivity and sensitivity compared with simpler designs.
    "Super heterodyne" is a contraction of "supersonic heterodyne", where "supersonic" indicates frequencies above the range of human hearing. The word heterodyne is derived from the Greek rootshetero- "different", and -dyne "power".

## Slide 3: BLOCK DIAGRAM OF A TYPICAL SUPERHETERODYNE RADIO RECEIVER

## Slide 4: LOCAL OSCILLATOR AND MIXER
The signal is then fed into a circuit where it is mixed with a sine wave from a variable frequency oscillator known as the LOCAL OSCILLATOR(LO).
The mixer uses a non-linear component to produce both sum and difference beat frequencies signals, each one containing the modulation contained in the desired signal.
In practice the RF and LO frequencies need to track closely but not perfectly.
The frequency of the local oscillator fLO is set so the desired reception radio frequency fRF mixes to fIF .
There are two choices for the local oscillator frequency because the dominant mixer products are at fRF ± fLO .
If the local oscillator frequency is less than the desired reception frequency. It is called LOW –SIDE INJECTION (fIF = fRF − fLO).
If the local oscillator is higher, then it is called HIGH SIDE INJECTION (fIF = fLO − fRF).

## Slide 5: INTERMEDIATE FREQUENCY AMPLIFIER
The stages of an intermediate frequency amplifier are tune to a fixed frequency that does not change as the receiving frequency changes.
The IF amplifier is selective around its center frequency fIF .
The choice has some performance advantages.
FIRST, it is easier and less expensive to get high selectivity at a lower frequency , for the same bandwidth, a tuned circuit at a lower frequency needs a lower Q. stated another way, for the same filter technology a higher center stages to achieve the same selectivity bandwidth.
SECOND , it is easier and less expensive to get high gain at a lower frequency.

## Slide 6: DEMODULATION
The received signal is now processed by the demodulator stage where the audio signal is recovered and then further amplified.
AM demodulator requires the simple rectification of the RF signal, and a simple RC low pass filter to remove remnants of the intermediate frequency.
Different demodulators are required for different types of transmission, and they include.
AM Diode detector and SYNCHRONOUS AM DETECTOR are required in demodulation process.

## Slide 7: ADVANTAGES AND DRAWBACKS OF THE SUPERHETERODYNE DESIGN
Super heterodyne receiver have essentially replaced all previous receiver designs.
The superhet receivers offers superior sensitivity, frequency stability and selectivity.
Compared with the tuned radio frequency receiver design, superhet’s offer better stability because tunable oscillator is more easily realized than a tunable amplifier.
Operating at a lower frequency , IF filters can give narrower pass bands at the same Q factor than an equivalent RF filter.
Regenerative and super regenerative receivers offered a high sensitivity. But often suffer from stability problems making them difficult to operate.

## Slide 8
Thank you