## Slide 1
Presentation On: Monochrome Television Receiver
Comilla University
Submitted To:
Md. Imran Hossain
Assistant Professor
Dept. of ICT
Comilla University
Submitted By:
ID:11809003
Dept. of ICT
Comilla University
Submission Time:23/11/2021

## Slide 2: Basics of Monochrome TV Receiver
Data transmitted by Monochrome TV transmitter antenna will be received by Monochrome TV receiver.
In Monochrome TV, display will be black and white with the shades of gray.

## Slide 3: Here, our agenda is…..
  Receive EM signal by Antenna at Rx,
  Convert that into Electrical signal
  Separate sound and video signals
  Play sound by speaker and Play video by tube

## Slide 4: Block Diagram of Monochrome TV receiver
Video Amplifier
RF Tuner
Common IF Amplifier
Video Detector
Scan & synch. circuit
Sound
Amplifier
Sound IF
Amplifier
FM Sound
Demodulator
Picture Tube
Light
Receiving Antenna
Speaker

## Slide 5: Working Process…..
Receiving antenna will receive electro magnetic signal and converts EM signal in RF electrical signal.
RF frequency will be here in terms of VHF and UHF.
In RF tuner , it translates RF frequency to IF frequency.

## Slide 6: Continued…
There are two intermediate frequency. One is for video and one is for audio.
IF frequency for sound will be 33.4 MHz.
IF frequency for picture will be 38.9 MHz.
For example In RF tuner, if local oscillator frequency is 101.15 MHz then you will be able to extract if frequency for pictures as well as sound.
After that, there will be Common IF Amplifier which will be amplifying picture IF frequency as well as sound IF frequency.

## Slide 7: Video Portion
And then we will be giving this to video detector.
In video portion, there will be Video Amplifier and that video amplifier will be connecting it with picture tube.
This picture tube that will be translating video information into light.
And in that there will be two types of scanning, horizontal scanning and vertical scanning.
So whatever electrical information that is given by video amplifier that will be translating horizontal to vertical scanning

## Slide 8: Continued…..
This video information that has been getting done by scanning horizontally and vertically.
We need to synchronize out with the data which is there in video signal. So for that we will be having synchronization over here.
in video detector there will be having amplitude demodulation and that demodulation signal that we will be giving it to video amplifier.
And that is what we are synchronizing with picture tube that will form picture over here.

## Slide 9: Sound Portion
For audio that audio intermediate frequency that we will be giving it to sound if amplifier and then after there will be FM demodulation.
After demodulation there will be audio signal over here and that audio signal will be weak.
So we will be again having sound amplifier and then that signal will be given to speaker so that speaker will generate sound

## Slide 10: Parameters of Monochrome TV Receiver
It has a video information, in between black and white with the shades of gray.
It Receives channels in the VHF and UHF.
Picture and sound signals are demodulated from RF carrier received from antenna.

## Slide 11: Thank You