## Slide 1: Presentation On Analog Communication Topic : AF Receiver
Submitted To
Md Imran Hossain
Assistant Professor Department Of ICT Comilla University, Cumilla.
Submitted By
Hridoy Chandra Das
ID:11809009 Session:2017-18
Dept. Of Ict Comilla University

## Slide 2: AF Receiver
The AM super heterodyne receiver takes the amplitude modulated wave as an input and produces the original audio signal as an output.
Sensitivity is the capacity of detecting RF signal and demodulating it, while at the lowest power level.

## Slide 3
RF Tuner Selector
RF-IF Converter (Mixer)
AM Demodulator
Audio Amplifier
IF Filter
Antenna
Audio Output
Loud Speaker

## Slide 4: RF Tuner Section
The amplitude modulated wave received by the antenna is first passed to the tuner circuit through a transformer. The tuner circuit is nothing but a LC circuit, which is also called as resonant or tank circuit.

## Slide 5: RF Mixer
The signal from the tuner output is sent to the RF-IF converter, which acts as a mixer. It has a local oscillator, which produces a constant frequency. The mixing process is done here, having the received signal as one input and the local oscillator frequency as the other input. The resultant output is a mixture of two frequencies[(f1+f2),(f1−f2)] produced by the mixer, which is called as the Intermediate Frequency (IF).

## Slide 6: IF Filter
Intermediate frequency filter is a band pass filter, which passes the desired frequency. It eliminates all other unwanted frequency components present in it. This is the advantage of IF filter, which allows only IF frequency.

## Slide 7: AM Demodulator
The received AM wave is now demodulated using AM demodulator. This demodulator uses the envelope detection process to receive the modulating signal.

## Slide 8: Audio Amplifier
This is the power amplifier stage, which is used to amplify the detected audio signal. The processed signal is strengthened to be effective. This signal is passed on to the loudspeaker to get the original sound signal.

## Slide 9: Thank You!