## Slide 1
Presentation On: SUPERHETRODYNE RECEIVER
Comilla University
Submitted To:
Md Imran Hossain
Assistant Professor,
Dept. of ICT
Comilla University
Submitted By:
Id:11809030
Dept. of ICT
Comilla University
Submission Time:23/11/2021

## Slide 2
A super heterodyne receiver converts all incoming
radio frequency (RF) signals to a lower frequency
known as an intermediate frequency (IF).
Also known as frequency conversion, high
frequency down converted to low frequency.(IF)

## Slide 3
Basics of Super Heterodyne Receiver
At high frequency, processing cost of circuit is high,
so we should do signal processing at low frequency.
At low frequency, transmission cost of signal is high with low bandwidth,
so signal transmission should be done at high frequency.
So, in super heterodyne receiver, we take care or above points
Signal transmission at high frequency
Signal processing at lower frequency

## Slide 4
2nd
Detector
RF Amplifier
Mixer or 1st
Detector
IF Amplifier
Audio
Amplifier
Local Oscillator
f LO = f RF + f 1F
f RF
f 1F (Diff)
Block Diagram of Super Heterodyne Receiver

## Slide 5
Sections
Heterodyne receiver has five sections
RF section
Mixer/converter section
IF section
Audio detector section
Audio amplifier section

## Slide 6: RF Section
Provide initial band Iimiting to prevent specific unwanted radio
frequency called image frequency from entering into receiver.
Reduces the noise bandwidth of the receiver and provides the initial
step toward reducing the over all receiver bandwidth to the
minimum bandwidth required to pass the information signal.

## Slide 7
The signal is then fed into a Circuit where it is mixed with a sine wave from
a variable frequency oscillator known as the LOCAL OSCILLATOR(LO).
The mixer uses a non-linear component to produce both sum and
difference beat frequencies signals, each one containing the modulation
contained in the desired signal.
The output of the mixer may include the original RF signal at f RF, the local
oscillator signal at fLO and the two new heterodyne frequencies f ER+f LO
and fER-f LO
LOCAL OSCILLATOR AND MIXER

## Slide 8
INTERMEDIATE FREQUENCY AMPLIFIER
The stages of an intermediate frequency amplifier are tune to a fixed frequency that does not change as the receiving frequency changes.
The IF amplifier is selective around its center frequency fIF
Typically the IF center frequency fIF is chosen to be less than the
desired reception frequency fRE

## Slide 9
Detector section
- To convert the IF signals back to the original
source information (demodulation).
- Can be as simple as a single diode or as complex
as a PLL or balanced demodulator.
Audio amplifier section
- Comprises several cascaded audio amplifiers and
one or more speakers

## Slide 10
Thank You