## Slide 1: Binary Arithmetic

## Slide 2: Adding Bits
1 + 1 = 2, but 2 should be represented as (10)2 in binary
Adding two bits: the sum is S and the carry is C
Adding three bits: the sum is S and the carry is C
X
+ Y
C S
0
+ 0
0 0
0
+ 1
0 1
1
+ 0
0 1
1
+ 1
1 0
1
0
+ 0
0 1
1
0
+ 1
1 0
1
1
+ 0
1 0
1
1
+ 1
1 1
0
0
+ 0
0 0
0
0
+ 1
0 1
0
1
+ 0
0 1
0
1
+ 1
1 0

## Slide 3: Binary Addition
Start with the least significant bit (rightmost bit)
Add each pair of bits
Include the carry in the addition, if present
0
0
0
1
1
1
0
1
0
0
1
1
0
1
1
0
+
(54)
(29)
(83)
1
carry
0
1
2
3
4
bit position:
5
6
7
1
1
1
0
1
0
1
0
0
1
1

## Slide 4: Subtracting Bits
Subtracting 2 bits (X – Y): we get the difference (D) and the borrow-out (B) shown as 0 or -1
Subtracting two bits (X – Y) with a borrow-in = -1: we get the difference (D) and the borrow-out (B)
X
– Y
B D
0
– 0
0 0
0
– 1
-1 1
1
– 0
0 1
1
– 1
0 0
-1
0
– 0
-1 1
-1
0
– 1
-1 0
-1
1
– 0
0 0
-1
1
– 1
-1 1
-1
X
– Y
B D
borrow-in

## Slide 5: Binary Subtraction
Start with the least significant bit (rightmost bit)
Subtract each pair of bits
Include the borrow in the subtraction, if present
0
0
0
1
1
1
0
1
0
0
1
1
0
1
1
0
–
(54)
(29)
(25)
0
1
2
3
4
bit position:
5
6
7
-1
-1
0
0
0
1
1
0
0
1
borrow
-1

## Slide 6: Binary Multiplication
Binary Multiplication table is simple:
0×0=0, 0×1=0, 1×0=0, 1×1=1
Multiplicand 11002 = 12
Multiplier × 11012 = 13
1100
0000
1100
1100
Product 100111002 = 156
n-bit multiplicand × n-bit multiplier = 2n-bit product
Accomplished via shifting and addition
Binary multiplication is easy
0 × multiplicand = 0
1 × multiplicand = multiplicand

## Slide 7: Hexadecimal Addition
Start with the least significant hexadecimal digits
Let Sum = summation of two hex digits
If Sum is greater than or equal to 16
  Sum = Sum – 16 and Carry = 1
Example:
A
F
C
D
B
0
1
1
1
9
C
3
7
2
8
6
5
1
3
9
5
E
8
4
B
+
5 + B = 5 + 11 = 16
Since Sum ≥ 16
Sum = 16 – 16 = 0
Carry = 1
0
1
carry

## Slide 8: Hexadecimal Subtraction
Start with the least significant hexadecimal digits
Let Difference = subtraction of two hex digits
If Difference is negative
  Difference = 16 + Difference and Borrow = -1
Example:
8
8
1
1
0
4
-1
9
C
3
7
2
8
6
5
1
3
9
5
E
8
4
B
-
Since 5 < B, Difference < 0
Difference = 16+5–11 = 10
Borrow = -1
A
-1
borrow
A
-1

## Slide 9: Shifting the Bits to the Left
What happens if the bits are shifted to the left by 1 bit position?
What happens if the bits are shifted to the left by 2 bit positions?
0
0
0
0
1
0
1
0
0
0
0
0
0
1
0
1
= 5
Before
After
= 10
0
0
0
1
0
1
0
0
0
0
0
0
0
1
0
1
= 5
Before
After
= 20
Shifting the Bits to the Left by n bit positions is multiplication by 2n
As long as we have sufficient space to store the bits
Multiplication
By 2
Multiplication
By 4

## Slide 10: Shifting the Bits to the Right
What happens if the bits are shifted to the right by 1 bit position?
What happens if the bits are shifted to the right by 2 bit positions?
0
0
0
1
0
0
1
1
0
0
1
0
0
1
1
0
= 38
Before
After
= 19, r=0
Shifting the Bits to the Right by n bit positions is division by 2n
The remainder r is the value of the bits that are shifted out
Division
By 2
Division
By 4
0
0
0
0
1
0
0
1
0
0
1
0
0
1
1
0
= 38
Before
After
= 9, r=2